## Slide 1: SEL Membrane Systems
By Lee Warwick
Contracts Manager

## Slide 2
Contents
Who are SEL?
Types of Membrane
Methods of Jointing
Drainage Pipe Connections
Membrane Protection
Quality Assurance

## Slide 3
Who are SEL?
SEL provide high quality, value-engineered solutions for SuDS and contaminated land remediation throughout the UK
Adopt an open-minded approach to developing site specific solutions
In-house stage 1 design capabilities (catchment analysis, sketch layouts, CAD)
Forge and maintain close relationships with leading academic institutions, key research bodies, specialist Consultants and manufacturers
Develop and manufacture a comprehensive range of unique products and bespoke components (flow controls, diffusers, prefab membranes)
Maintain a highly skilled and specialised workforce together with bespoke plant and equipment

## Slide 4
Types of Membrane
LLDPE
PE
PP
HDPE
Reinforced membranes

## Slide 5
Types of Membrane
HDPE
  High density polyethylene.
  High density polyethylene (HDPE) geomembrane liners are used in a wide range of containment applications. This material provides excellent durability and chemical resistance properties and is reliable in exposed applications, has ultraviolet protection and ageing resistance from the intense stresses of weather. This is a very stiff membrane.
  Various thicknesses and large roll sizes available.
  Usually has welded joints.

## Slide 6
Types of Membrane
LLDPE
  Linear low density polyethylene
  Provides much of the same durability and resistance properties found in high density polyethylene (HDPE) geomembranes, but with the added benefit of increased material flexibility because it is a lower-density polymer.
  Various thicknesses and large roll sizes available.
  Usually has welded joints.

## Slide 7
Types of Membrane
PE
  Polythene
  Polythene sheet is more commonly used as a damp-proof membrane.
  Normally 1200 gauge thick (0.25mm) and supplied in rolls 4 m wide by 25 m long.
  Usually has taped joints

## Slide 8
Types of Membrane
PP
  Polypropylene
  Outstanding flexibility, elongation (up to 700% before rupture), cold temperature resistance, long term UV stability, and advanced chemical resistance. Polypropylene is one of the most flexible membranes available for use as a fabricated geomembrane, making detail work such as creating corners an easy task.
  Various thicknesses and large roll sizes available.
  Usually has welded joints.

## Slide 9
Types of Membrane
Reinforced membranes
  Usually laminated carrier and scrim (grid)
  All the benefits of the membrane but with added strength and puncture resistance of the scrim (grid). Very low elongation.
  Various thicknesses and large roll sizes available.
  Usually has welded joints.

## Slide 10
Methods of Jointing
Hot air gun
Extrusion
Tape
Twin wedge welder
Lap

## Slide 11
Methods of Jointing
Twin wedge welder

## Slide 12
Methods of Jointing
Twin wedge welder

## Slide 13
Methods of Jointing
Twin wedge welder – Testing, 1 bar/mm thickness for 5 minutes

## Slide 14
Methods of Jointing
Hot air gun

## Slide 15
Methods of Jointing
Hot air gun – Testing
55 PSI minimum
5mm nozzle.
<100mm from seam
Traversed at c.12m/min

## Slide 16: Methods of Jointing
Extrusion welding
  Extruding molten plastic
  Suitable for PE membranes where hot air welding is not suitable
  Relatively slow and therefore expensive compared to other jointing methods

## Slide 17: Methods of Jointing
Extrusion welding
  Spark test

## Slide 18: Methods of Jointing
Tape
  Needs dry and clean surface
  Cannot test joint
  Limitations under hydrostatic pressure

## Slide 19: Methods of Jointing
Lap
  Usually minimum 300mm
  Only suitable where watertightness is not an issue i.e. leaky tank
  Fast and cost effective where appropriate
  “Token gesture”

## Slide 20: Drainage Pipe Connections
Robust
Fit Standard Drainage
Watertight

## Slide 21: Drainage Pipe Connections
Example of bad workmanship

## Slide 22: Drainage Pipe Connections
Example of good workmanship

## Slide 23: Drainage Pipe Connections
PVOD Components

## Slide 24: Drainage Pipe Connections
PVOD Components

## Slide 25: Membrane Protection
Outer layer around membrane
Occasionally on inside of membrane
Prevent puncture during installation and backfilling
Non-woven, needle punched
Minimum 300g/m²

## Slide 26: Membrane Protection

## Slide 27: Quality Assurance
ISO9001
  Quality Plan
  On site CQA

## Slide 28: Quality Assurance
Quality Plan

## Slide 29: Quality Assurance
On site CQA

## Slide 30: Any Questions?...
SEL Environmental Ltd
Lee Warwick 07711 377602
l.warwick@selenvironmental.com
www.selel.co.uk